## Slide 1: PRPL mesh
Overview

## Slide 2: Executive summary
Intel has contributed its mesh framework into prplMesh
  Designed for production-quality with very strict security requirement
  Intel invested many man years to develop, test, document, flow diagrams,…
  Includes a proven full Mesh solution (Controller & Agent running on actual HW)
Intel will support prpl
  Training/Bootcamp and on-going support
  Dedicated team contributor/maintainers to keep developing with PRPL
PRPL own the project and will adapt it into prplMesh
  Convert flows to EasyMesh standard, certify

## Slide 3: PrplMesh - System arch partitioning

## Slide 4: PRPL EasyMesh architecture
PRPL mesh Agent
Platform
Service
1905
.
1
Topology
&
discovery service
1905
.
1
Transport
service
OS
/
Distribution Management Entity
PRPL mesh Controller
BTL
BTL
Local Message Bus
(
XSub
-
XPub
)
PAL
TFL
TFL
BWL
Hostapd
Supplicant
Netlink
BML
TFL
WLAN Driver
(
cfg
80211
)
BML
–
BeeRocks Management Library
BTL
–
BeeRocks Transport Library
(
TX
/
RX CMDU
)
BWL
–
BeeRocks WLAN Library
D
-
WPAL
–
Dynamic WLAN Platform Library
Sheared
Library
TFL
–
TLV factory Library
PAL
–
Platform Abstraction Library
PPL
–
Platform Plugin Library
MPL
–
Management Plugin Library
PPL
Network Stack
L
2
–
Raw Socket
TFL
TFL
Management
Service
OS
/
Distribution
FAPI
D
-
WPAL
WLAN
API
Management
API
?
s
MPL
Algorithms
Algorithms
Features
Multi
-
AP Framework
Local BUS IPC
Legend
API
Framework
WLAN
Controller/agent

## Slide 5: Main benefits of PRPL’s new EasyMesh stack (1/3)
Fully featured Mesh solution (including Controller)
  Includes optimized and tested Controller decision-making algorithms
  Working and tested Mesh system
    mobility / steering, channel selection, statistics, network map, BH optimization, DFS
Security - Intel requires very strict security standards
  Solution arch complies with Intel’s strict security requirements for product grade
    Threat model approval, service and permission segregation (compartmentalization), security code reviews, malware scans, static code analysis and more…

## Slide 6: Main benefits of PRPL’s new EasyMesh stack (2/3)
IEEE 1905.1 stack
  Tested Intel proprietary stack, built for 32bit systems with all EasyMesh features
    fragmentation, MID tracking, cookie, multicast, etc..
Scalable architecture
  Designed to be easily ported to multiple SDK’s / Wi-Fi vendors / HW platforms
    Using Platform, Wi-Fi and Management Adaptation Libraries
    Already quickly ported to RDK-B (running) from UGW (OpenWRT-based)
  Micro-Service approach
    Best fit for open source with dispersed community of multiple developers / geos

## Slide 7: Main benefits of PRPL’s new EasyMesh stack (3/3)
  TLV Factory Library
    Major infrastructure capability, enabling automatic creation of 1905 message TLV Classes
      Replaces monolithic BBF 1905 with a bus-based service (also used for IPC)
    Designed to easily add / modify message structures
      All R1 messages supported
      R2 messages can be added trivially
      YAML inputs converted into C++ Classes with APIs to form & parse 1905 messages & TLVs
      Internal messaging reuses the TLV factory (via YAML)
      Serializes into any specific structure (unlike Google ProtoBuf) such as 1905
        Valuable as standalone open-source

## Slide 8: PRPL mesh agent/controller – high level overview

## Slide 9: High-level Agent Architecture

## Slide 10: High-level Controller Architecture

## Slide 11: BACKUP

## Slide 12: Integration markup
Based on Intel presentation
MultiAP Framework
Kernel
bridge / Switchdev / OpenvSwitch 3
ioctl
SIOCETHTOOL
SIOCGIFHWADDR
netlink
RTNLGRP_LINK
SIOCGIFINDEX
RTM_GETLINK
* Controller can be on remote device and may be accessed indirectly through the transport according to EasyMesh standard
OS specific
implementation
Mesh controller*
Mesh Agent
Northbound API
Management Service
1905.1 Topology & discovery service
1905.1 transport service
Platform Service
PPL
Local Message Bus (XSub-XPub)
Network Stack L2 - raw socket
MPL
Ethernet
Bridge
Westbound API
hostapd
wpa_supplicant
nl80211
Wireless
Southbound API
BWL
WPA_ctrl wrapper
Southbound API
Southbound API
Mesh SW upgrade controller*
Mesh SW upgrade agent
SW upgrade API
System IPC

## Slide 13: EasyMesh - Local BUS IPC